## Slide 1: Co-existence of legacy and P4-offloaded 5G UPF deployments using open-source software
Apostolos Prassas
Georgios P. Katsikas
Kostis Trantzas
Christos Tranoris

## Slide 2: Importance of UPF
User plane function (UPF) is the data plane anchor of 5G
Separates control and user planes
Allows (high-performance) data forwarding
Acts as a policy enforcement point
Provides support for network slicing
Allows local 5G traffic breakout (MEC, low latency)
Provides implementation flexibility and programmability

## Slide 3: The problem
Legacy UPFs are deployed on general-purpose CPUs
Struggle to meet high-performance standards (uRLLC, eMBB)

## Slide 4: The need
To offload traffic from demanding slices into hardware
...without losing the flexibility of software-based deployments

## Slide 5: Objectives

## Slide 6: Objectives
Offload the UPF dataplane into the network
Exploit high performance network equipment
Provide a fast equivalent to legacy kernel-based UPFs
1
Design a closed-loop service to automate UPF offloading
2
Monitor events coming from 5GC (e.g., slice requests)
Act by instructing TFS to deploy P4-accelerated UPFs
Ensure that legacy and offloaded UPFs can co-exist
3
Integrate both with an end-to-end open-source 5G (OAI)

## Slide 7: Challenges

## Slide 8: Challenges
Hide the complexity of a P4-based UPF from the end user
1
UPF
Low-level P4 instructions
UPF Connectivity Service
High-level Service intent
Pick the right tools to allow easy testing
2
gnbsim
emulates
5G gNB
bmv2
Tofino
TNA
mimic
End-to-end integration with an open 5GC (OAI)
Equivalence with real physical deployments

## Slide 9: Background in 5G
And the role of UPF

## Slide 10: Simplified 5G architecture around UPF
5GC
5G gNB
Data Network
5G UPF
DL
UL
DL
UL
N4
N6
N3
GTP tunnel
PFCP
To I-UPF
N9
5G UE

## Slide 11: Methodology

## Slide 12: A Closed-loop Architecture
Open 5G
implementation
5GC
DNN 1 Internet
Legacy UPF

## Slide 13: A Closed-loop Architecture
Open 5G
implementation
5GC
DNN 2 Intranet
UPF
Open 5G UPF implementation
DNN 1 Internet
Legacy UPF

## Slide 14: A Closed-loop Architecture
Orchestration Platform
Closed-loop design
Open 5G
implementation
Specific UE slice request
event
action
5GC
DNN 2 Intranet
UPF
Open 5G UPF implementation
DNN 1 Internet
Legacy UPF
Provision offloaded UPF

## Slide 15: Relation with ETSI

## Slide 16: Why is this relevant for ETSI SDGs?
What is new? | Relevance with ETSI SDGs and other open-source projects and/or standards
Integration between ETSI OSL and ETSI TFS via the TFS NBI | 
Integration between OAI (SD-Fabric version) and Prometheus | 
Exploit the ETSI OSL integration with telemetry engine (OSL metrico) | 
New capabilities and bug fixes introduced at the TFS SBI P4 driver | 
1x new TFS P4 services for UPF offloading based on SD-Fabric (NEW!) | 
TFS integration with Stratum-based P4 switches (i.e., bmv2) | 
A closed-loop among all these systems (NEW!) | 

## Slide 17: UPF Implementation
The P4 SD-Fabric dataplane

## Slide 18
ACL
Next
UPF Ingress
UPF pipeline of tables for uplink (UL)
5G gNB
ΕΤΗ
IPv4
UDP
GTP
IPv4
ICMP
2152
dp-1:
10.10.1.1
2152
10.10.1.1
10.10.1.2
10.10.2.2
12.1.1.2
dp-2:
10.10.2.1
DNN 2
UE 12.1.1.2 pings 10.10.2.2
5G UE
Filtering
ingress_port_vlan
fwd_classifier
interfaces
uplink_sessions
uplink_terminations
uplink_recirc_rules
ig_tunnel_peers
miss
miss
Forwarding
bridging
Pre-Next
next_vlan
next (hashed)
acl
ΕΤΗ
IPv4
ICMP
10.10.2.2
12.1.1.2
GTP
applications
miss
QoS
set_slice_tc
Egress Next
egress_vlan
miss
miss
default_tc
queues
miss
UPF

## Slide 19
UPF Egress
ACL
Next
UPF Ingress
UPF pipeline of tables for downlink (DL)
ΕΤΗ
IPv4
UDP
GTP
IPv4
ICMP
2152
dp-2:
10.10.2.1
2152
10.10.1.2
10.10.1.1
12.1.1.2
10.10.2.2
dp-1:
10.10.1.1
DN replies with ICMP echo reply
Filtering
ingress_port_vlan
fwd_classifier
interfaces
downlink_sessions
downlink_terminations
ig_tunnel_peers
Forwarding
bridging
Pre-Next
next_vlan
next (hashed)
acl
QoS
set_slice_tc
Egress Next
egress_vlan
ΕΤΗ
IPv4
ICMP
12.1.1.2
10.10.2.2
GTP
DNN 2
5G UE
5G gNB
applications
miss
gtpu_encap
eg_tunnel_peers
miss
miss
default_tc
queues
miss
miss
UPF

## Slide 20: Scenario

## Slide 21: Scenario

## Slide 22: Scenario
VM #1
UEs
gNB
AMF
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
DNN 1 Internet

## Slide 23: Scenario
VM #1
UEs
gNB
AMF
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 Users
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UEs
gNB
P4-offloaded 5G UPF
DNN 1 Internet
VM #2
GTP-U
P4Runtime
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1

## Slide 24: Scenario
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 Users
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UEs
gNB
VM #5
Service Orchestrator
Closed-loop Service
P4-offloaded 5G UPF
DNN 1 Internet
VM #2
GTP-U
P4Runtime
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions

## Slide 25: Workflow
1
Initial system state
Clean state OSL, TFS, 5GC, P4 switch, Prometheus
3
Introduce silver-class UEs
Traffic handling through legacy UPF
Service design
4
Introduce gold-class UE
Policy action
Event handling
2
Closed-loop service design and ordering
Metrics of interest
Event trigger
Traffic handling through legacy UPF

## Slide 26: Initial System State
1

## Slide 27
VM #1
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1

## Slide 28
VM #1
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
Browse OSL Marketplace
1
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1

## Slide 29
VM #1
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
2
TFS clean state
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1

## Slide 30
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
3
Deploy 5GC
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1

## Slide 31
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
Legacy UPF’s DNN is the Internet
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1

## Slide 32
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
SD-Fabric UPF is up
SD-Fabric UPF’s DNN is the Intranet (10.10.2.2)
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1

## Slide 33
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
Deploy a Stratum-based P4 switch
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
No P4 program is installed
4

## Slide 34
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
A Monitoring service is pre-installed
5G Telemetry
5

## Slide 35: Initial System State – Demo

## Slide 36: Closed-loop Service Design & Ordering
2

## Slide 37
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
5G Telemetry
5G Monitoring service gets events from the 5GC
TFS Controller service invokes a P4 UPF via the TFS service API
5G Monitoring events
Actions
1

## Slide 38
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
5G Telemetry
Order the P4-offloaded 5G UPF Service
5G Monitoring events
Actions
2

## Slide 39: Designed Closed-loop – Demo

## Slide 40: Introduce Silver-class UEs
The legacy UPF in action
3

## Slide 41
VM #1
AMF
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
5G Telemetry
5G Monitoring events
Actions

## Slide 42
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
Deploy a silver-class UE + gNB
1

## Slide 43
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
Metric “# of Silver UEs”=1 in OpenSlice
2

## Slide 44
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
UE#1: ping google
pkt
3

## Slide 45
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
Deploy another silver-class UE + gNB
4

## Slide 46
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
Metric “# of Silver UEs”=2 in OpenSlice
5

## Slide 47
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
UE#2: ping google
6
pkt

## Slide 48: Introduce Silver-class UEs

## Slide 49: Introduce a Gold-class UE
TFS and the P4 UPF in action
4

## Slide 50
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions

## Slide 51
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
Deploy a gold-class UE + gNB
1

## Slide 52
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
2
Delay Metric propagation in OpenSlice
Freeze the time

## Slide 53
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
3
UE#3: ping 10.10.2.2
pkt
Ping fails because the
P4 switch runs nothing!

## Slide 54
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
4
TFS is still in clean state

## Slide 55
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
5a
Metric “# of Gold UEs”=1 in OpenSlice
OpenSlice instructs TFS to deploy the P4 UPF service
5b

## Slide 56
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
DNN 1 Internet
VM #2
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
TFS connects to the switch and translates UPF service into P4 rules
P4-offloaded 5G UPF
P4Runtime
6
GTP-U

## Slide 57
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
P4-offloaded 5G UPF
DNN 1 Internet
VM #2
GTP-U
P4Runtime
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
7
UE#3: ping 10.10.2.2
pkt

## Slide 58
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
P4-offloaded 5G UPF
DNN 1 Internet
VM #2
GTP-U
P4Runtime
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
8a
UE#3: ping 10.10.2.2
pkt
UE#1 and UE#2: ping google
pkt
pkt
8b

## Slide 59
VM #1
UEs
gNB
AMF
5G Telemetry
Slice 1 Users
SMF
UDM
UDR
Legacy UPF
SD-Fabric UPF (CP)
Slice 2 User
AUSF
NRF
5G Core
5G Monitoring events
Control Plane path
Data Plane path
Closed-loop path
SD-Fabric UPF Controller
PFCP Agent
TFS plugin
VM #4
VM #3
DNN Intranet
P4Runtime
SDN Controller
UE
gNB
VM #5
Service Orchestrator
Closed-loop Service
P4-offloaded 5G UPF
DNN 1 Internet
VM #2
GTP-U
P4Runtime
dp-1
10.10.1.2
N6
dp-1
10.10.2.2
DNN 2
Intranet
N3
dp-2
10.10.2.1
dp-1
10.10.1.1
Actions
Tear Stratum switch down
pkt
pkt
9
pkt

## Slide 60: Introduce a Gold-class UE

## Slide 61: Team behind the PoC

## Slide 62: Contributors
Georgios P. Katsikas NSS Technical Leader
Kostis Trantzas ETSI OSL TSC Chair
Apostolos Prassas NSS TM + Soft. Engineer
Christos Tranoris ETSI OSL LG Chair

## Slide 63: Acknowledgements
EU-funded Research and Development
HORIZON-JU-SNS-2022 ACROSS project with grant agreement number 101097122
Check our demo out!

## Slide 64: Thank You! TFSsupport@etsi.org
Georgios P. Katsikas NSS Technical Leader ETSI TFS TSC member ETSI OSL TSC member
gkatsikas at ubitech dot eu
Apostolos Prassas NSS TM Soft. Engineer